## Slide 1
Lab 1: Vitis HLS and the seven-segment display
Seven-segment decoder as a first HLS design
Customized Embedded Processors Lab · Chair of Embedded Systems (CES)
Vitis HLS 2022.2 · Vivado 2022.2 · Blackboard Zynq-7000 (xc7z007sclg400-1)

## Slide 2
Section A — Initial setup
Access the machine, load the toolchain, create the first HLS project.

## Slide 3: Lab objective and tool flow
▪ Goal of Lab 1.1: get the Xilinx 2022.2 toolchain running and create a working Vitis HLS project.
▪ Goal of Lab 1.2: describe a small hardware function in C/C++ and let Vitis HLS generate the RTL.
▪ No VHDL and no Verilog is written in this lab. The decoder logic comes from C/C++.
▪ Vivado is only opened and verified in Lab 1 — it is used for real in Lab 2.
C/C++ function → C simulation → C synthesis → RTL + reports → exported IP
│
Lab 2: Vivado block design → bitstream
Tool roles. Vitis HLS turns C/C++ into an RTL IP block. Vivado builds the system around that IP and produces the bitstream. Vitis builds the software that runs on the ARM core.

## Slide 4: Repository structure
▪ One directory per task, our recommendation is under <Xilinx_app>/lab1_task2
▪ Create your Vitis HLS / Vivado projects outside the tool installation directory, in your own writable working directory.
▪ Keep every lab artfact under one tree — incomplete submissions are usually a directory problem, not a design problem.

## Slide 5
On the lab computers, the Xilinx software suite is usually located under: /Software/xilinx/<version>
If you cannot able to find the Xilinx software, you can use this convenience command:
find /Software /tools /opt /usr /home -maxdepth 8 -type f \( -name vivado -o -name vitis -o -name vitis_hls \) 2>/dev/null | sort
The `settings64.sh` script configures the current terminal session to use the Xilinx toolchain. This script sets environment variables such as PATH, LD_LIBRARY_PATH, XILINX_VIVADO, and XILINX_VITIS to ensure the terminal can locate the correct version of Vivado, Vitis, or Vitis HLS. You must source the script rather than run it normally, because the changes need to persist within the same shell session. This ensures that, even if multiple Xilinx versions are installed on the same machine, the specific version to be used is explicitly selected.

## Slide 6: Starting Vitis HLS 2022.2
vitis_hls &
▪ The & keeps the shell usable while the GUI runs.
▪ The Welcome page confirms both the GUI and X11 forwarding work.
▪ If the window never appears: check echo $DISPLAY and xdpyinfo.
▪ Choose Create Project — do not open an existing project yet.

## Slide 7: New project: name, location, sources
▪ Project name lab1_task2_hls; location = your lab working directory. No spaces in the path.
▪ Design files: seven_segment.cpp, seven_segment.h
▪ Testbench files: seven_segment_tb.cpp — added on the separate testbench page, not with the design files.
▪ Vitis HLS copies nothing: the files stay where they are and are referenced by path.

## Slide 8: Solution settings: top function, part, clock
Design files: Leave blank
Testbench files: Leave blank
Solution: Create
▪ Top function = the C/C++ function that becomes the hardware block. Everything it calls is synthesized with it.
▪ Solution name solution1, Flow target: Vivado IP Flow Target.
▪ Clock period 20 ns (50 MHz) and part xc7z007sclg400-1 — the Blackboard Zynq-7000 device.
▪ Wrong part or wrong clock here means the reports and the exported IP are useless later.
At the initial configuration, we do not need to add any files to the Vitis HLS Project Wizard screens.

## Slide 9: Starting Vivado 2022.2
vivado &
▪ In Lab 1 Vivado is only opened to prove the installation and the GUI work.
▪ Confirm the title bar reads 2022.2 — mixed versions break IP hand-over between HLS and Vivado.
▪ Close it again; no Vivado project is created in Lab 1.
Lab 2 preview. The IP you export at the end of Lab 1 is imported into a Vivado block design in Lab 2.1.

## Slide 10: Setup verification
[ok] logged in on the assigned lab machine
[ok] lab working directory exists and is writable
[ok] repository checked out, task directories visible
[ok] Xilinx 2022.2 environment sourced
[ok] vitis_hls -version and vivado -version both report 2022.2
[ok] X11 forwarding works, both GUIs open
[ok] Vitis HLS project created with top function and part configured
[next] Lab 1.2 — implement the seven-segment decoder
▪ If any line above fails, fix it before writing code. Do not debug HLS on a broken environment.
▪ Record machine name, tool version and working directory in your notes — the first question in the oral check.

## Slide 11
Section B — Lab 1.2: Seven-segment decoder
From a C/C++ function to synthesized RTL.

## Slide 12: What this lab is about
You write a C++ function. Vitis HLS turns it into real hardware (RTL).
The function is not software: after synthesis it becomes a block with input and output wires.
Target: drive the Blackboard's four-digit seven-segment display.
No Verilog and no VHDL is written anywhere in this lab.
C++ function -> C simulation -> C synthesis -> RTL + reports -> exported IP
|
Lab 2: Vivado block design -> board
Note: Tool roles. Vitis HLS turns C/C++ into an IP block. Vivado builds the system around it. Vitis builds the software that runs on the ARM core.

## Slide 13: Task : Seven-segment decoder using HLS
▪ Implement a two-digit decimal display decoder in C/C++.
▪ Convert an input value from 0 to 99 into two seven-segment patterns.
▪ Verify the design using C simulation.
▪ Synthesize the function into RTL using Vitis HLS.
Input value (0 … 99)
↓
C/C++ HLS function: seven_segment()
↓
Tens digit and ones digit
↓
Two seven-segment patterns

## Slide 14: The display: four digits, one bus
Conceptual view: AXI-side registers driving the multiplexed seven-segment decoder. We will get into AXIs on Lab2.
Seven segments (A…G) plus a decimal point form one digit.
The board has four digits, but they share one 8-bit segment bus.
an[3:0] selects which digit is currently connected to that bus.
Segments and anodes are both active-low: a 0 turns something on.

## Slide 15: You cannot show two digits at once At any single instant, only one digit can be lit + but the scan makes all four appear lit simultaneously to the eye
Important: If two anodes are enabled at the same time, both digits receive the same pattern. Displaying 4 and 2 simultaneously is physically impossible.
The display is driven by time multiplexing: light one digit, then the next, quickly.
At ~1 ms per digit the eye blends them into one steady four-digit number.
So the block must remember which digit it is currently driving.
time ──►
an0 lit, seg = pattern of "2" (1 ms)
an1 lit, seg = pattern of "4" (1 ms)
an2 lit, seg = blank (1 ms)
an3 lit, seg = blank (1 ms) … repeats 250x per second

## Slide 16: Combinational vs. clocked
A combinational function has no memory: its output depends only on its inputs right now.
Such a function can never scan, because scanning needs a notion of “later”.
In HLS, static local variables become registers — they keep their value between clock cycles.
With ap_ctrl_none the block is free-running: its body executes once every clock cycle.
static ap_uint<16> tick = 0; // counts cycles inside one digit slot
static ap_uint<2> pos = 0; // which digit is lit right now
Note: pos is 2 bits wide, so 3 + 1 wraps to 0 on its own: the scan runs 0 → 1 → 2 → 3 → 0 forever.

## Slide 17: Which bit drives which segment
The constraints file (XDC) fixes this mapping — it is not a free choice:
seg[0] = SSEG_CA (A) seg[4] = SSEG_CE (E)
seg[1] = SSEG_CB (B) seg[5] = SSEG_CF (F)
seg[2] = SSEG_CC (C) seg[6] = SSEG_CG (G)
seg[3] = SSEG_CD (D) seg[7] = SSEG_DP (decimal point)
static const unsigned SEG_A = 1u << 0; // … through …
static const unsigned SEG_G = 1u << 6;
case 1: return SEG_B | SEG_C; // | (right bar)
case 7: return SEG_A | SEG_B | SEG_C; // ‾|
Important: Get the bit order wrong and the display lies. If A lands in the wrong bit, every pattern is mirrored: 2 appears as 5, 6 as 9. Symmetric digits such as 0 and 8 hide the mistake.

## Slide 18: Driving the anodes
Only one anode may be low at any instant — that is the whole idea of the scan.
A single-digit design would hardcode an = 0b1110 (digit 0 always on).
The four-digit version is that same constant, shifted to the active position:
*an = ~(ap_uint<4>(1) << pos);
pos | an | digit lit
0 | 1110 | rightmost (ones)
1 | 1101 | tens
2 | 1011 | hundreds
3 | 0111 | leftmost (thousands)

## Slide 19: Putting it together
void seven_segment(ap_uint<14> value, ap_uint<8> *seg, ap_uint<4> *an) {
#pragma HLS INTERFACE ap_none port=value
#pragma HLS INTERFACE ap_none port=seg
#pragma HLS INTERFACE ap_none port=an
#pragma HLS INTERFACE ap_ctrl_none port=return
#pragma HLS PIPELINE II=1
/* advance tick / pos */
/* pick the digit belonging to this position */
/* blank the leading zeros */
/* drive seg and an */
}
value is 0…9999. Two digits are the standard case; three and four come for free.
Leading zeros are blanked, so 42 shows as ··42, not 0042.

## Slide 20: The testbench
The synthesized function has no cin, no scanf, no file I/O, none of that is hardware (and not supported in Vitis HLS).
The testbench is plain C++ that calls the function and checks its outputs.
It uses fixed values, so any failure is reproducible.
unsigned int values[] = {0, 7, 42, 99, 100, 9999};
To observe a full scan it calls the function ~200 000 times and records which pattern each anode received.
It also asserts that exactly one anode is active in every single cycle.
Note: Interactive input arrives in Lab 2.2, from a C program on the ARM processor — never from the testbench.

## Slide 21: Creating the Vitis HLS project
New Vitis HLS Project: solution name, clock period, part, flow target
source /Software/xilinx/2022.2/Vitis_HLS/2022.2/settings64.sh
vitis_hls &
Design files: seven_segment.cpp, seven_segment.h
Testbench: seven_segment_tb.cpp — added on the separate testbench page.
Top function seven_segment; part xc7z007sclg400-1; clock 20 ns (50 MHz).

## Slide 22: C simulation
C simulation compiles the function as ordinary C++ — no hardware is generated yet.
It answers one question: is the digit-to-pattern mapping correct?
It runs your fixed test vectors and reports pass or fail.
$ Run C Simulation
seven_segment test passed
CSim done with 0 errors
Important: C simulation cannot see timing. Everything on the next slide is invisible here.

## Slide 23: C synthesis — and the number that matters
Synthesis summary: Timing Estimate and Interval in the Performance & Resource table
Check Interval = 1: the block performs one execution per clock cycle.
Without #pragma HLS PIPELINE II=1 the tool spreads the body over ~35 cycles. The scan then runs 35× too slowly and the display flickers visibly.
Also check: estimated clock under 20 ns, and no BRAM or DSP for a decoder.
Note: This is the lesson of the lab. The C simulation passes either way. Only the synthesis report reveals the problem.

## Slide 24: Exporting the IP
Export RTL dialog: format Vivado IP (.zip)
Solution → Export RTL, format Vivado IP (.zip).
Verify afterwards that solution1/impl/export.zip and solution1/impl/ip/component.xml exist.
This exported IP is exactly what Lab 2 imports into a Vivado block design.

## Slide 25: Checklist
✓ Vitis HLS project created, part and clock configured
✓ Segment table written from the XDC pin mapping
✓ Scan implemented with static tick / pos registers
✓ Anodes driven as ~(1 << pos), exactly one active at a time
✓ C simulation passes on the fixed vectors
✓ Synthesis report checked: Interval = 1, timing met
✓ IP exported
[next] Lab 2 — the same block, controlled by the processor over AXI
Reference result | Value
Interval (II) | 1
Estimated Fmax | ~111 MHz (target 50 MHz)
BRAM / DSP | 0 / 0
Note: Deliverables. The three source files, the synthesis report, the exported IP, and a short answer to: why does this display need a clock at all?