## Slide 1
Lab 2: A calculator in HLS
From an HLS function to an AXI4-Lite IP driven by software
Customized Embedded Processors Lab · Chair of Embedded Systems (CES)
Vitis HLS · Vivado · Vitis 2022.2 · Blackboard Zynq-7000 (xc7z007sclg400-1)

## Slide 2: Lab 2 goal
System view: ARM core → AXI → seven-segment controller → display
You type two numbers and an operation into a terminal.
The ARM processor sends them to your HLS block over AXI4-Lite.
The block computes the result and shows it on the seven-segment display.
Still no Verilog: the arithmetic and the display logic are both C++.

## Slide 3: Lab 2.1: HLS IP creation + Vivado block design integration
Start from Lab 1.2 seven-segment HLS design
1
Modify it into an AXI4-Lite controlled HLS IP
2
Run C synthesis
3
Export as Vivado IP
4
Open Vivado, create Zynq block design
5
Import the exported HLS IP
6
Connect it through AXI Interconnect
7
Assign address range
8
Validate design
9
Generate wrapper / bitstream / hardware export
10
Main output:
A Zynq system where the seven_segment_axi IP is connected to the Processing System through AXI.

## Slide 4: Lab 2.2: C driver / software-side control
Open Vitis
Create or use exported hardware platform
Write a C application
Access the seven_segment_axi registers from software
Write digit values through AXI
Observe the seven-segment display output
Optionally loop through values 0–9
Main output:
A C program running on the ARM processor controls the HLS-generated seven-segment peripheral.
Main output:
A C program running on the ARM processor controls the HLS-generated seven-segment peripheral.

## Slide 5: HLS: new source files for Lab 2
▪ New HLS project, then create new files — do not add the Lab 1 files as linked resources.
▪ seven_segment_axi.cpp and seven_segment_axi.h; copy the Lab 1 decoder body into them.
▪ Lab 1 stays untouched and still works; Lab 2 evolves independently.
▪ A testbench is optional here — C simulation may be skipped and you go straight to C synthesis.

## Slide 6: What actually changes from Lab 1
Lab 1 | Lab 2
one input: value | three inputs: op1, op2, op_sel
#pragma ... ap_none port=value | #pragma ... s_axilite port=op1 #pragma ... s_axilite port=op2 #pragma ... s_axilite port=op_sel + arithmetic (switch statement, magnitude/sign handling) and two extra display-selection branches for the minus sign and error dash
segment table | IDENTICAL
active-low conversion | IDENTICAL
tick / pos scan registers | IDENTICAL
*an = ~(1 << pos) | IDENTICAL
#pragma HLS PIPELINE II=1 | IDENTICAL
Note: This is the point of the lab. If your Lab 1 works, Lab 2 is three pragmas plus the arithmetic. The display half is not rewritten — it is reused.

## Slide 7: The new interface
void seven_segment_axi(ap_uint<7> op1, ap_uint<7> op2, ap_uint<2> op_sel,
ap_uint<8> *seg, ap_uint<4> *an) {
#pragma HLS INTERFACE s_axilite port=op1 bundle=CTRL
#pragma HLS INTERFACE s_axilite port=op2 bundle=CTRL
#pragma HLS INTERFACE s_axilite port=op_sel bundle=CTRL
#pragma HLS INTERFACE ap_none port=seg
#pragma HLS INTERFACE ap_none port=an
#pragma HLS INTERFACE ap_ctrl_none port=return
#pragma HLS PIPELINE II=1
Only the three inputs are memory-mapped. seg and an stay plain wires.
ap_ctrl_none keeps the block free-running, so the display never stops scanning.
Operands are 0…99; op_sel selects the operation.

## Slide 8: AXI4-Lite?
The ARM core cannot call hardware like a C function. The block must look like memory.
Software writes to an address; the fabric decodes it and hands the value to your logic.
AXI4-Lite fits: a handful of control registers, no streaming bandwidth needed.
Interface | Use
Full AXI4 | high-performance burst transfers
AXI4-Lite | simple register access — this lab
AXI4-Stream | continuous data, no addresses
ARM processor → AXI Interconnect → AXI4-Lite slave (HLS IP) → display

## Slide 9: The arithmetic, and its edge cases
switch (op_sel) {
case OP_ADD: result = op1 + op2; break; // 0
case OP_SUB: result = op1 - op2; break; // 1
case OP_MUL: result = op1 * op2; break; // 2
default: // 3 = divide
if (op2 == 0) error = true; // no defined result
else result = op1 / op2;
}
Negative results (subtraction) show a leading minus sign — segment G alone.
Division by zero and anything that will not fit shows ----.
The display always has a defined state: hardware cannot throw an exception.
Note: Range check: 99 × 99 = 9801 still fits on four digits, so multiplication never overflows here.

## Slide 10: The register map
After synthesis, Vitis HLS generates xseven_segment_axi_hw.h:
Offset | Register
0x00 … 0x0c | reserved
0x10 | op1
0x18 | op2
0x20 | op_sel
Important: Because the block is ap_ctrl_none, there is no ap_start register. The software never starts the block and never polls for completion — it only writes these three values.
Always read these offsets from the generated header, never guess them.

## Slide 11: HLS: synthesize and export the IP
▪ Project → Project Settings → Synthesis: top function seven_segment_axi, then Run C Synthesis.
▪ The report must show an AXI4-Lite slave named s_axi_CTRL and note the digit offset (0x10) — you need it in software.
▪ Export as Vivado IP (.zip); Display Name seven_segment_axi, Taxonomy /UserIP.
▪ Verify solution1/impl/export.zip and solution1/impl/ip/component.xml.

## Slide 12
▪ Project → Project Settings → Synthesis: top function seven_segment_axi, then Run C Synthesis.
▪ The report must show an AXI4-Lite slave named s_axi_CTRL and note the digit offset (0x10). You need it in software.
▪ Export as Vivado IP (.zip); Display Name seven_segment_axi, Taxonomy /UserIP.
▪ Verify solution1/impl/export.zip and solution1/impl/ip/component.xml.

## Slide 13
Select the export format:
- Vivado IP (.zip)
Keep the default output location unless a custom export path is required. Default output is usually generated under:
solution1/impl/export.zip
solution1/impl/ip/
Let’s fill in the IP configuration fields:
- Vendor: ces.kit.edu
- Library: hls
- Version: 1.0
- Description: AXI4-Lite controlled seven-segment display HLS IP
- Display Name: seven_segment_axi
- Taxonomy: /UserIP
- Click OK to export the generated RTL as a Vivado IP.
After export, verify that the following files/directories were generated:
- solution1/impl/export.zip
- solution1/impl/ip/component.xml
The exported IP will be imported into Vivado.

## Slide 14: Vivado: project and constraints
New RTL project, part xc7z007sclg400-1, no design sources.
Add the Blackboard XDC: it maps seg[7:0] and an[3:0] to the display pins.
No extra Verilog or VHDL is added in this lab — the anode logic lives in the HLS block.
seg[0] → K14 (SSEG_CA) … seg[7] → K18 (SSEG_DP)
an[0] → K19 (SSEG_AN0) … an[3] → L16 (SSEG_AN3)
Note: This is why the scan was written in HLS: the block design stays simple, and the lab never asks you to write RTL.

## Slide 15: Vivado: block design
Block design after Run Connection Automation: ZYNQ7 PS → AXI Interconnect → seven_segment_axi_0/s_axi_CTRL
Create Block Design, add ZYNQ7 Processing System, then Run Block Automation.
Settings → IP → Repository: add the exported solution1/impl/ip directory.
Add IP → seven_segment_axi from the catalog under UserIP.
Run Connection Automation to wire AXI, clock and reset.

## Slide 16: Vivado: external ports and address
Right-click seg / an → Make External; Address Editor: s_axi_CTRL at 0x4000_0000
Right-click the seg and an pins → Make External.
Address Editor: assign s_axi_CTRL to 0x4000_0000, range 64K.
Important: Naming matters. The external ports must be exactly seg and an to match the XDC. If Vivado creates seg_0, rename it in External Port Properties.

## Slide 17: Vivado: build and export
Create HDL Wrapper, then Run Synthesis → Implementation → Generate Bitstream.
File → Export → Export Hardware, include bitstream → seven_segment_wrapper.xsa.
synthesis = netlist · implementation = place & route + timing · bitstream = FPGA configuration
Important: Whenever the HLS code changes, the IP must be re-exported, the block design refreshed (Report IP Status → Upgrade), and the bitstream and XSA regenerated. A stale XSA is the most common reason a working design misbehaves on the board.

## Slide 18: Vitis: platform and application
Create Application Project: processor ps7_cortexa9_0, Empty Application
Platform project from seven_segment_wrapper.xsa, then Build Project.
Application project seven_segment_app, processor ps7_cortexa9_0, standalone, empty.
The XSA tells Vitis which processor exists and where your IP is mapped — platform first.

## Slide 19: Vitis: the software
#define CALC_BASEADDR XPAR_SEVEN_SEGMENT_AXI_0_S_AXI_CTRL_BASEADDR
#define OP1_REG_OFFSET 0x10
#define OP2_REG_OFFSET 0x18
#define OPSEL_REG_OFFSET 0x20
op1 = read_operand("First number"); /* over the terminal */
op2 = read_operand("Second number");
op_sel = read_operation();
Xil_Out32(CALC_BASEADDR + OP1_REG_OFFSET, op1);
Xil_Out32(CALC_BASEADDR + OP2_REG_OFFSET, op2);
Xil_Out32(CALC_BASEADDR + OPSEL_REG_OFFSET, op_sel);
Three writes, and the display updates on the very next clock cycle.
Use the generated base-address macro from xparameters.h — never a literal address.
Validate the operands in software too: a 7-bit register silently truncates 100 to 4.

## Slide 20: Run on the board
Vitis: right-click seven_segment_app → Run As → Launch on Hardware
Run As → Launch on Hardware: Vitis programs the bitstream, then starts the ELF.
Open a serial terminal at 115200 baud to type the operands.
Try 40 + 2 → 42, then 5 - 9 → -4, then 7 / 0 → ----.
✓ AXI4-Lite IP exported
✓ block design validated
✓ bitstream and XSA generated
✓ platform + application built
✓ operands accepted over the terminal
✓ result correct on the display

## Slide 21: Checklist and deliverables
✓ Lab 1 display block reused unchanged
✓ three AXI4-Lite pragmas added, top function renamed
✓ arithmetic implemented, division by zero handled
✓ Interval = 1 confirmed in the synthesis report
✓ IP exported, imported, address assigned
✓ bitstream and XSA regenerated from the current IP
✓ software writes op1 / op2 / op_sel and the display follows
Reference result | Value
HLS Interval (II) | 1, Fmax ~81 MHz
Post-route timing | WNS +12.7 ns, 0 failing endpoints
Utilisation | 7.4 % LUT, 4.1 % FF, 1 DSP, 0 BRAM
Bonded I/O | 12 (8 segment + 4 anode)
Note: Deliverables. The HLS sources, the block design, the XSA, the Vitis application, a board demo, and a short answer to: which registers does the software write, and what does the hardware compute?