## Slide 1
Lab 2: A calculator in HLS
The Lab 1 display block, now driven by the processor
Customized Embedded Processors Lab · Chair of Embedded Systems (CES)
Vitis HLS · Vivado · Vitis 2022.2 · Blackboard Zynq-7000 (xc7z007sclg400-1)

## Slide 2
Lab 2 goal
img/02-system-overview.png
Block diagram: ARM PS → AXI Interconnect → seven_segment_axi → four-digit display
▪ You type two numbers and an operation into a terminal.
▪ The ARM processor sends them to your HLS block over AXI4-Lite.
▪ The block computes the result and shows it on the seven-segment display.
▪ Still no Verilog: the arithmetic and the display logic are both C++.
1

## Slide 3
What actually changes from Lab 1
Lab 1 Lab 2
-------------------------------- --------------------------------
one input: value three inputs: op1, op2, op_sel
#pragma ... ap_none port=value #pragma ... s_axilite port=op1
#pragma ... s_axilite port=op2
#pragma ... s_axilite port=op_sel
+ one switch statement (the maths)
segment table IDENTICAL
active-low conversion IDENTICAL
tick / pos scan registers IDENTICAL
*an = ~(1 << pos) IDENTICAL
#pragma HLS PIPELINE II=1 IDENTICAL
This is the point of the lab. If your Lab 1 works, Lab 2 is three pragmas plus the arithmetic. The display half is not rewritten — it is reused.
2

## Slide 4
Why AXI4-Lite?
▪ The ARM core cannot call hardware like a C function. The block must look like memory.
▪ Software writes to an address; the fabric decodes it and hands the value to your logic.
▪ AXI4-Lite fits: a handful of control registers, no streaming bandwidth needed.
Interface | Use
Full AXI4 | high-performance burst transfers
AXI4-Lite | simple register access — this lab
AXI4-Stream | continuous data, no addresses
ARM processor → AXI Interconnect → AXI4-Lite slave (HLS IP) → display
3

## Slide 5
The new interface
void seven_segment_axi(ap_uint<7> op1, ap_uint<7> op2, ap_uint<2> op_sel,
ap_uint<8> *seg, ap_uint<4> *an) {
#pragma HLS INTERFACE s_axilite port=op1 bundle=CTRL
#pragma HLS INTERFACE s_axilite port=op2 bundle=CTRL
#pragma HLS INTERFACE s_axilite port=op_sel bundle=CTRL
#pragma HLS INTERFACE ap_none port=seg
#pragma HLS INTERFACE ap_none port=an
#pragma HLS INTERFACE ap_ctrl_none port=return
#pragma HLS PIPELINE II=1
▪ Only the three inputs are memory-mapped. seg and an stay plain wires.
▪ ap_ctrl_none keeps the block free-running, so the display never stops scanning.
▪ Operands are 0…99; op_sel selects the operation.
4

## Slide 6
The arithmetic, and its edge cases
switch (op_sel) {
case OP_ADD: result = op1 + op2; break; // 0
case OP_SUB: result = op1 - op2; break; // 1
case OP_MUL: result = op1 * op2; break; // 2
default: // 3 = divide
if (op2 == 0) error = true; // no defined result
else result = op1 / op2;
}
▪ Negative results (subtraction) show a leading minus sign — segment G alone.
▪ Division by zero and anything that will not fit shows ----.
▪ The display always has a defined state: hardware cannot throw an exception.
Range check: 99 × 99 = 9801 still fits on four digits, so multiplication never overflows here.
5

## Slide 7
The register map
After synthesis, Vitis HLS generates xseven_segment_axi_hw.h:
Offset | Register
0x00 … 0x0c | reserved
0x10 | op1
0x18 | op2
0x20 | op_sel
Because the block is ap_ctrl_none, there is no ap_start register. The software never starts the block and never polls for completion — it only writes these three values.
▪ Always read these offsets from the generated header, never guess them.
6

## Slide 8
Synthesize and export
img/08-synth-axi-interface.png
Synthesis report Interface table showing the s_axi_CTRL ports plus seg / an, and Interval = 1
▪ Top function seven_segment_axi, part xc7z007sclg400-1, clock 20 ns.
▪ The report must show an AXI4-Lite slave named s_axi_CTRL, and seg / an as ap_none.
▪ Confirm Interval = 1 again — same flicker trap as Lab 1.
▪ Export RTL as Vivado IP; verify solution1/impl/ip/component.xml.
7

## Slide 9
Vivado: project and constraints
▪ New RTL project, part xc7z007sclg400-1, no design sources.
▪ Add the Blackboard XDC: it maps seg[7:0] and an[3:0] to the display pins.
▪ No extra Verilog or VHDL is added in this lab — the anode logic lives in the HLS block.
seg[0] → K14 (SSEG_CA) … seg[7] → K18 (SSEG_DP)
an[0] → K19 (SSEG_AN0) … an[3] → L16 (SSEG_AN3)
This is why the scan was written in HLS: the block design stays simple, and the lab never asks you to write RTL.
8

## Slide 10
Vivado: block design
img/10-block-design.png
Diagram after Run Connection Automation: ZYNQ7 PS → AXI Interconnect → seven_segment_axi_0/s_axi_CTRL
▪ Create Block Design, add ZYNQ7 Processing System, then Run Block Automation.
▪ Settings → IP → Repository: add the exported solution1/impl/ip directory.
▪ Add IP → seven_segment_axi from the catalog under UserIP.
▪ Run Connection Automation to wire AXI, clock and reset.
9

## Slide 11
Vivado: external ports and address
img/11-external-ports.png
Right-click seg / an → Make External, plus the Address Editor showing s_axi_CTRL at 0x4000_0000
▪ Right-click the seg and an pins → Make External.
▪ Address Editor: assign s_axi_CTRL to 0x4000_0000, range 64K.
Naming matters. The external ports must be exactly seg and an to match the XDC. If Vivado creates seg_0, rename it in External Port Properties.
10

## Slide 12
Vivado: build and export
▪ Create HDL Wrapper, then Run Synthesis → Implementation → Generate Bitstream.
▪ File → Export → Export Hardware, include bitstream → seven_segment_wrapper.xsa.
synthesis = netlist · implementation = place & route + timing · bitstream = FPGA configuration
Whenever the HLS code changes, the IP must be re-exported, the block design refreshed (Report IP Status → Upgrade), and the bitstream and XSA regenerated. A stale XSA is the most common reason a working design misbehaves on the board.
11

## Slide 13
Vitis: platform and application
img/13-vitis-projects.png
Create Platform Project from the XSA, then New Application Project on ps7_cortexa9_0, Empty Application
▪ Platform project from seven_segment_wrapper.xsa, then Build Project.
▪ Application project seven_segment_app, processor ps7_cortexa9_0, standalone, empty.
▪ The XSA tells Vitis which processor exists and where your IP is mapped — platform first.
12

## Slide 14
Vitis: the software
#define CALC_BASEADDR XPAR_SEVEN_SEGMENT_AXI_0_S_AXI_CTRL_BASEADDR
#define OP1_REG_OFFSET 0x10
#define OP2_REG_OFFSET 0x18
#define OPSEL_REG_OFFSET 0x20
op1 = read_operand("First number"); /* over the terminal */
op2 = read_operand("Second number");
op_sel = read_operation();
Xil_Out32(CALC_BASEADDR + OP1_REG_OFFSET, op1);
Xil_Out32(CALC_BASEADDR + OP2_REG_OFFSET, op2);
Xil_Out32(CALC_BASEADDR + OPSEL_REG_OFFSET, op_sel);
▪ Three writes, and the display updates on the very next clock cycle.
▪ Use the generated base-address macro from xparameters.h — never a literal address.
▪ Validate the operands in software too: a 7-bit register silently truncates 100 to 4.
13

## Slide 15
Run on the board
img/15-board-result.png
Terminal showing the entered operands next to a photo of the display holding the result
▪ Run As → Launch on Hardware: Vitis programs the bitstream, then starts the ELF.
▪ Open a serial terminal at 115200 baud to type the operands.
▪ Try 40 + 2 → 42, then 5 - 9 → -4, then 7 / 0 → ----.
[ok] AXI4-Lite IP exported [ok] platform + application built
[ok] block design validated [ok] operands accepted over the terminal
[ok] bitstream and XSA generated [ok] result correct on the display
14

## Slide 16
Checklist and deliverables
[ok] Lab 1 display block reused unchanged
[ok] three AXI4-Lite pragmas added, top function renamed
[ok] arithmetic implemented, division by zero handled
[ok] Interval = 1 confirmed in the synthesis report
[ok] IP exported, imported, address assigned
[ok] bitstream and XSA regenerated from the current IP
[ok] software writes op1 / op2 / op_sel and the display follows
Reference result | Value
HLS Interval (II) | 1, Fmax ~81 MHz
Post-route timing | WNS +12.7 ns, 0 failing endpoints
Utilisation | 7.4 % LUT, 4.1 % FF, 1 DSP, 0 BRAM
Bonded I/O | 12 (8 segment + 4 anode)
Deliverables. The HLS sources, the block design, the XSA, the Vitis application, a board demo, and a short answer to: which registers does the software write, and what does the hardware compute?
15