## Slide 1
Lab 1: Vitis HLS and the seven-segment display
Describing hardware in C++ instead of Verilog
Customized Embedded Processors Lab · Chair of Embedded Systems (CES)
Vitis HLS 2022.2 · Blackboard Zynq-7000 (xc7z007sclg400-1)

## Slide 2
What this lab is about
▪ You write a C++ function. Vitis HLS turns it into real hardware (RTL).
▪ The function is not software: after synthesis it becomes a block with input and output wires.
▪ Target: drive the Blackboard's four-digit seven-segment display.
▪ No Verilog and no VHDL is written anywhere in this lab.
C++ function → C simulation → C synthesis → RTL + reports → exported IP
│
Lab 2: Vivado block design → board
Tool roles. Vitis HLS turns C/C++ into an IP block. Vivado builds the system around it. Vitis builds the software that runs on the ARM core.
1

## Slide 3
The display: four digits, one bus
img/03-seven-segment-board.png
Photo or diagram of the Blackboard display, segments labelled A…G and the four digit positions labelled an0…an3
▪ Seven segments (A…G) plus a decimal point form one digit.
▪ The board has four digits, but they share one 8-bit segment bus.
▪ an[3:0] selects which digit is currently connected to that bus.
▪ Segments and anodes are both active-low: a 0 turns something on.
2

## Slide 4
You cannot show two digits at once
If two anodes are enabled at the same time, both digits receive the same pattern. Displaying 4 and 2 simultaneously is physically impossible.
▪ The display is driven by time multiplexing: light one digit, then the next, quickly.
▪ At ~1 ms per digit the eye blends them into one steady four-digit number.
▪ So the block must remember which digit it is currently driving.
time ──►
an0 lit, seg = pattern of "2" (1 ms)
an1 lit, seg = pattern of "4" (1 ms)
an2 lit, seg = blank (1 ms)
an3 lit, seg = blank (1 ms) … repeats 250x per second
3

## Slide 5
Combinational vs. clocked
▪ A combinational function has no memory: its output depends only on its inputs right now.
▪ Such a function can never scan, because scanning needs a notion of "later".
▪ In HLS, static local variables become registers — they keep their value between clock cycles.
▪ With ap_ctrl_none the block is free-running: its body executes once every clock cycle.
static ap_uint<16> tick = 0; // counts cycles inside one digit slot
static ap_uint<2> pos = 0; // which digit is lit right now
pos is 2 bits wide, so 3 + 1 wraps to 0 on its own: the scan runs 0 → 1 → 2 → 3 → 0 forever.
4

## Slide 6
Which bit drives which segment
The constraints file (XDC) fixes this mapping — it is not a free choice:
seg[0] = SSEG_CA (A) seg[4] = SSEG_CE (E)
seg[1] = SSEG_CB (B) seg[5] = SSEG_CF (F)
seg[2] = SSEG_CC (C) seg[6] = SSEG_CG (G)
seg[3] = SSEG_CD (D) seg[7] = SSEG_DP (decimal point)
static const unsigned SEG_A = 1u << 0; // … through …
static const unsigned SEG_G = 1u << 6;
case 1: return SEG_B | SEG_C; // | (right bar)
case 7: return SEG_A | SEG_B | SEG_C; // ‾|
Get the bit order wrong and the display lies. If A lands in the wrong bit, every pattern is mirrored: 2 appears as 5, 6 as 9. Symmetric digits such as 0 and 8 hide the mistake.
5

## Slide 7
Driving the anodes
▪ Only one anode may be low at any instant — that is the whole idea of the scan.
▪ A single-digit design would hardcode an = 0b1110 (digit 0 always on).
▪ The four-digit version is that same constant, shifted to the active position:
*an = ~(ap_uint<4>(1) << pos);
pos | an | digit lit
0 | 1110 | rightmost (ones)
1 | 1101 | tens
2 | 1011 | hundreds
3 | 0111 | leftmost (thousands)
6

## Slide 8
Putting it together
void seven_segment(ap_uint<14> value, ap_uint<8> *seg, ap_uint<4> *an) {
#pragma HLS INTERFACE ap_none port=value
#pragma HLS INTERFACE ap_none port=seg
#pragma HLS INTERFACE ap_none port=an
#pragma HLS INTERFACE ap_ctrl_none port=return
#pragma HLS PIPELINE II=1
/* advance tick / pos */
/* pick the digit belonging to this position */
/* blank the leading zeros */
/* drive seg and an */
}
▪ value is 0…9999. Two digits are the standard case; three and four come for free.
▪ Leading zeros are blanked, so 42 shows as ··42, not 0042.
7

## Slide 9
The testbench
▪ The synthesized function has no cin, no scanf, no file I/O — none of that is hardware.
▪ The testbench is plain C++ that calls the function and checks its outputs.
▪ It uses fixed values, so any failure is reproducible.
unsigned int values[] = {0, 7, 42, 99, 100, 9999};
▪ To observe a full scan it calls the function ~200 000 times and records which
pattern each anode received.
▪ It also asserts that exactly one anode is active in every single cycle.
Interactive input arrives in Lab 2.2, from a C program on the ARM processor — never from the testbench.
8

## Slide 10
Creating the Vitis HLS project
img/10-hls-create-project.png
Create Project wizard: project name, then the Add Sources page showing the design and testbench files
source /Software/xilinx/2022.2/Vitis_HLS/2022.2/settings64.sh
vitis_hls &
▪ Design files: seven_segment.cpp, seven_segment.h
▪ Testbench: seven_segment_tb.cpp — added on the separate testbench page.
▪ Top function seven_segment; part xc7z007sclg400-1; clock 20 ns (50 MHz).
9

## Slide 11
C simulation
img/11-csim-passed.png
Console after Run C Simulation showing "seven_segment test passed" and "CSim done with 0 errors"
▪ C simulation compiles the function as ordinary C++ — no hardware is generated yet.
▪ It answers one question: is the digit-to-pattern mapping correct?
▪ It runs your fixed test vectors and reports pass or fail.
C simulation cannot see timing. Everything on the next slide is invisible here.
10

## Slide 12
C synthesis — and the number that matters
img/12-synthesis-interval.png
Synthesis Summary with the Timing and Latency tables visible, the Interval column highlighted
▪ Check Interval = 1: the block performs one execution per clock cycle.
▪ Without #pragma HLS PIPELINE II=1 the tool spreads the body over ~35 cycles.
The scan then runs 35× too slowly and the display flickers visibly.
▪ Also check: estimated clock under 20 ns, and no BRAM or DSP for a decoder.
This is the lesson of the lab. The C simulation passes either way. Only the synthesis report reveals the problem.
11

## Slide 13
Exporting the IP
img/13-export-ip.png
Export RTL dialog, format Vivado IP, and the resulting solution1/impl/ip/component.xml
▪ Solution → Export RTL, format Vivado IP (.zip).
▪ Verify afterwards that solution1/impl/export.zip and
solution1/impl/ip/component.xml exist.
▪ This exported IP is exactly what Lab 2 imports into a Vivado block design.
12

## Slide 14
Checklist
[ok] Vitis HLS project created, part and clock configured
[ok] segment table written from the XDC pin mapping
[ok] scan implemented with static tick / pos registers
[ok] anodes driven as ~(1 << pos), exactly one active at a time
[ok] C simulation passes on the fixed vectors
[ok] synthesis report checked: Interval = 1, timing met
[ok] IP exported
[next] Lab 2 — the same block, controlled by the processor over AXI
Reference result | Value
Interval (II) | 1
Estimated Fmax | ~111 MHz (target 50 MHz)
BRAM / DSP | 0 / 0
Deliverables. The three source files, the synthesis report, the exported IP, and a short answer to: why does this display need a clock at all?
13