## Slide 1
Lab 3 — Pragma-Based Design-Space Exploration
How to take a DNN kernel from plain C to a working accelerator
Customized Embedded Processors Lab · Vitis HLS 2022.2 · Blackboard (xc7z007s)

## Slide 2: What this lab is about
Labs 1 and 2 had you write RTL directly — the VHDL was, more or less, the circuit you got.
This lab works one level up: you write C/C++, and Vitis HLS turns it into RTL for you.
The target is a DNN building block — the multiply-accumulate loops at the core of every neural-network layer, and the kind of workload this lab's accelerator work will build on.
Task 3.1: get a small DNN kernel synthesizing, no optimisation. Task 3.2: apply three specific pragmas and see exactly what each one buys you.

## Slide 3: Pragmas are not just better C
C is sequential which means that one statement finishes before the next starts. Hardware doesn't have to be, since several things can happen on the same clock edge.
Turning your C into RTL means inventing an architecture with how many adders, how many memory ports, what runs in parallel or in which schedule. Plain C gives the tool no basis to be ambitious.
A pragma is a directive that tells the compiler how to build it, parallelize this loop, duplicate this hardware, split this memory without changing what the code computes.
Today we will learn three pragmas, each aimed at a different part of that architecture decision.

## Slide 4: The pragma toolbox is more than three
Loop transformation — PIPELINE (overlap iterations), UNROLL (duplicate the loop body). Today's focus.
Memory — ARRAY_PARTITION (split a memory for parallel access), ARRAY_RESHAPE (repacks into wider words). Partitioning is also today's focus.
Interface — INTERFACE: how the function talks to the outside world (AXI, simple ports, …).
Task level — DATAFLOW: lets whole functions or loops overlap, not just iterations within one loop.
Also worth knowing — INLINE, LATENCY, ALLOCATION, LOOP_TRIPCOUNT.
Full reference: Vitis HLS User Guide (UG1399), chapter “HLS Pragmas.” Or just type #pragma HLS in the editor — autocomplete lists the rest. Vitis HLS Introductory Examples Github repository

## Slide 5: PIPELINE
A pipeline lets iteration N+1 of a loop start before iteration N finishes, in assembly line, not one part at a time.
It goes inside the loop body, right after the for statement.
prod: for (int k = 0; k < N; k++) {
#pragma HLS PIPELINE II=1
acc += A[i][k] * B[k][j];
}
▪ II (initiation interval) is the main knob. II=1 means a new iteration starts every clock cycle, the usual goal.
▪ You can pipeline a whole function too by putting the pragma right after its opening brace instead of inside a loop.

## Slide 6: UNROLL
Unroll makes N physical copies of the loop body, so N iterations really happen at once on N separate pieces of hardware instead of one piece reused N times.
It goes same place as PIPELINE, inside the loop.
prod: for (int k = 0; k < N; k++) {
#pragma HLS UNROLL factor=4
acc += A[i][k] * B[k][j];
}
▪ Leave out factor and the loop unrolls completely so that every iteration gets its own hardware. Fine for a loop of 4; reckless for a loop of 4000.
▪ More hardware only helps if it can all be fed at once which is exactly what the next pragma is for.

## Slide 7: ARRAY_PARTITION
The problem is that an on-chip memory (BRAM) usually has one or two ports. Unroll a loop that reads an array four times per iteration, and three of your four new multipliers sit idle waiting for memory.
It splits one array into several smaller memories (or plain registers), so several elements can be read in the same cycle.
data_t B[N][N];
#pragma HLS ARRAY_PARTITION variable=B type=cyclic factor=4 dim=2
▪ type=cyclic interleaves elements across partitions; type=block splits into contiguous chunks; type=complete gives every element its own register.
▪ Rule of thumb: partition the dimension your unrolled loop indexes, matching the factor to the unroll factor.

## Slide 8: Finding your way around Vitis HLS
You don't have to memorise pragma syntax: right-click a loop in the source view → Insert Directive lets you add PIPELINE / UNROLL / ARRAY_PARTITION from a menu, and it writes the pragma into your source for you.
Run C Simulation first, it always checks your C++ is correct, on your machine's own CPU, before you spend minutes synthesizing it.
Run C Synthesis to produce the report. It lands under [solution]/syn/report/ and also opens automatically in the GUI.
Two sections matter here: “Performance Estimates” (latency, II) and “Utilization Estimates” (BRAM/DSP/FF/LUT, and % of the device). Everything else you can ignore for now.

## Slide 9: Where to find a starting kernel
You are not expected to write a DNN layer in C from the scratch; you can start from something that already exists.
AMD/Xilinx's own example repository ships small, synthesizable Vitis HLS kernels, including matrix-multiply variants with pragmas already applied: Vitis HLS Introductory Examples (layout on the next slide).
If you are starting from an actual trained network, hls4ml and Xilinx's FINN both convert a trained Keras/PyTorch model into synthesizable HLS C++.
Pick something whose innermost loop runs more than ~8 times and reads an array more than once per iteration, otherwise there's nothing for UNROLL/PARTITION to show.

## Slide 10: Reading the repository layout
Every category below is a folder; every example folder has its own README, source, testbench, and a Tcl/Python run script, you can study the whole approach, not just borrow a file.
Vitis-HLS-Introductory-Examples/
Array/ ARRAY_PARTITION examples
array_partition_complete/ <- matmul kernel, today's reference
array_partition_block_cyclic/
Pipelining/ PIPELINE examples
Functions/hier_func/
Loops/pipelined_loop/
DSP/ FFT, FIR filters
Interface/ AXI / port examples
Task_level_Parallelism/ DATAFLOW examples
Today's default starting point: Array/array_partition_complete. ARRAY_PARTITION is already applied there; you add PIPELINE and UNROLL yourself.

## Slide 11: Getting the code onto the lab machine
The lab machines most likely don't have git, therefore you don't need a whole repository, just one file.
On GitHub, open the file and click “Raw”: that URL is the file's plain-text contents, nothing else. curl or wget will fetch it directly:
curl -O https://raw.githubusercontent.com/Xilinx/Vitis-HLS-Introductory-Examples/master/Array/array_partition_complete/matmul_partition.cpp
▪ If git is available, a shallow sparse checkout gets you one folder without the repository's full history:
git clone --depth 1 --filter=blob:none --sparse <repo-url>
git sparse-checkout set path/to/folder

## Slide 12
Getting a baseline on the board
No pragmas beyond what the interface needs
Task 3.1

## Slide 13: Task 3.1: find and fetch a kernel
Browse a source, the Xilinx repo and its layout (previous slides), or an hls4ml/FINN output
Picked a file? Pull just that one open it on GitHub, click “Raw”, then fetch the URL directly, no git required:
curl -O https://raw.githubusercontent.com/Xilinx/Vitis-HLS-Introductory-Examples/master/Array/array_partition_complete/matmul_partition.cpp
▪ If the folder has a matching header or testbench, grab those the same way, check the file listing on GitHub first.

## Slide 14: Task 3.1: build and record the baseline
Create a new Vitis HLS project; add the file(s) you downloaded as the design source, plus a testbench, reuse one if it came with the kernel, otherwise write a short one against a known input/output pair.
Run C Simulation, confirm the kernel computes the right answer before you touch performance at all.
Run C Synthesis with no pragmas beyond what the interface strictly needs.
Open the synthesis report and record latency (cycles), and DSP / BRAM / FF / LUT utilization, counts and percentages.
That's your baseline. Every Task 3.2 result gets compared against it.

## Slide 15
Exploring pragma combinations
PIPELINE · UNROLL · ARRAY_PARTITION, alone and combined
Task 3.2

## Slide 16: Task 3.2: step by step
Add PIPELINE to the innermost loop. Re-synthesize; note what changed, and why.
Undo that, add UNROLL instead, try a couple of factors. Re-synthesize; note what changed.
Add ARRAY_PARTITION on the array(s) the unrolled loop reads, factor matched to the unroll factor. Re-synthesize.
Combine PIPELINE + UNROLL + ARRAY_PARTITION. Re-synthesize.
For every variant: what you added, and in terms of the hardware, and why it changed what it changed.
Want to see a pragma already in use first? Pipelining/ has PIPELINE examples, Array/ has ARRAY_PARTITION examples (repo layout, slide 10). UNROLL usually shows up alongside one of the two; search the source for '#pragma HLS UNROLL'.

## Slide 17: Where Vitis HLS fits
Vitis HLS only gets you from C++ to RTL, plus the estimate you're reading in the report, it does not put anything on the board.
The RTL it produces becomes an IP block for a Vivado project which is the same tool you already used in Labs 1 and 2.
Vivado is where logic synthesis, implementation (place & route), and bitstream generation actually happen and where a design that “fits” in the HLS report can still fail, if the estimate was optimistic.
For this lab, C synthesis is enough since you're comparing pragma choices, not producing a bitstream. Keep the rest of the flow in mind regardless.
C/C++ -> Vitis HLS (C-sim, C-synthesis) -> RTL / IP -> Vivado (synth, impl, bitstream) -> FPGA

## Slide 18: What to hand in
A completed results table with baseline plus every pragma variant you tried, latency and utilization for each.
One or two sentences per pragma with what you added, and what changed in the hardware as a result.
The source file(s) you used, and where they came from.
A short explanation which configuration you would actually put on the board, and why.